## Slide 1: BRASS Scenario 6
Updates to MDL Schema and Software
Adapted from a flight test that occurred in 2015

## Slide 2: Scenario #6 – Brief Description
The MDL schema has updated from v0.8.17 to v0.8.19, and software is patchily adjusting for the change. The configuration management software is still on v0.8.17, but must configure and communicate with devices using v0.8.19 for the latest round of flight tests.
V0.8.17
V0.8.19

## Slide 3: Scenario #6 – Brief Description
There must be a pathway to deliver a v0.8.19 file to the DAU from the v0.8.17 configuration manager to set up the device, and reverse the communication when exporting the configuration from the device for verification.

## Slide 4: Test Article
Aircraft: C-12 Huron
By US Navy - navair.navy.mil, Public Domain, https://commons.wikimedia.org/w/index.php?curid=62352668

## Slide 5: Range Infrastructure
Range Network: Typical large military range e.g. Edwards Air Force Flight Test Center
Equipment Used:
  GSE (Ground Support Equipment)
Equipment Available:
  Existing instrumentation hardware

## Slide 6: Flight Test Operation Flow
Existing v0.8.17 configuration
Update to v0.8.19
Configure DAU
Export configuration
Downgrade to v0.8.17

## Slide 7: Associated Constraints
Configurations must be valid for their target version
Identical functional information must be expressed
  Textual representation will vary

## Slide 8: High Level Differences (From Changelog)
Time as a measurement
  DataAttributesType Added TimeAttributes for describing time as a Measurement
  Added MeasurementTimeRef so a Measurement can identify the associated time Measurement
  MeasurementTypeEnum: Added Time as an option
Tweaked VendorConfig and GenericParameters to allow xsd:any without violating XSD 1.0 rules.
PortType: Added various port attributes
DeviceType: Fixed Sensitivity and Excitation to allow multiple ConditionParameter elements

## Slide 9: High Level Differences (From Changelog)
Added GenericParameter to ChildType
Updated to latest TMATS schema
Added generic Parent/Child relationships with the Children element
Added handoff rule strings, exact format is tbd
Removed obsolete LinkControlMode from RadioLink
Settled on bit for fundamental unit. Removed Byte and BytePerSecond
Converted many enumerations to extensible enumerations
Describing a-priori time offsets in Packages
InternalStructure: Generalized Module concept for all NetworkNodes and Devices, added RunningApps element to describe mapping of TMAs to the modules
ModelNumber and SerialNumber: harmonized across schema to Model and SerialIdentifier

## Slide 10: Classic Solution
Hand update files for configuring devices
Hand validate files exported by device
No automatic solution

## Slide 11: Suggested Solutions
Batch update/downgrade MDL files when moving between dialects
Intercept database access calls and replace with current version equivalents (or approximations, as necessary)

## Slide 12: Supporting Files
MDL v0.8.17 and v0.8.19 schemas and examples
Example XSLT scripts previously used to translate between those versions
  Explicit description of what is different between the versions
  May be a spoiler if your techniques are looking to generate something similar e.g. based on the schema differences
    Bidirectional scripts do not exist for all versions of interest, so this cannot be relied on in all cases